Place your programme code here
[Arial Bold; 10,5pt.]
Example
O2.4-123
A Portable Experimental Buoy for Coastal Acoustic Monitoring as a Potential Complement to the IMS Hydroacoustic Network: Applications on the Argentinian Continental Shelf
Prario, I. Bos, P. Marques Rojo, R. Cinquini,M. Blanc, S.
Argentinian Navy Research Office & UNIDEF (CONICET)
Presentation Date: 11 September 2025

---
T1.3 - 299
A Portable Experimental Buoy for Coastal Acoustic Monitoring
Prario, I; Bos, P; Marques Rojo, R; Cinquini, M; Blanc, S.
Experimental Acoustic Buoy Platform
This custom-designed buoy is a prototype platform developed for the deployment of hydroacoustic instrumentation in a coastal environment.
It features:
A GRP (glass-reinforced plastic) hull for corrosion resistance and lightweight performance.
A solar power system to support autonomous operations.
A sealed electronics compartment and a central mast for sensors, antennas, and GPS.
Designed to withstand harsh marine conditions, including strong currents and waves up to 4 meters.

---
Cost-Effective Embedded System Design Using Off-the-Shelf Components
This custom-designed buoy is a prototype platform developed for the deployment of hydroacoustic instrumentation in a coastal environment.
It features:
A GRP (glass-reinforced plastic) hull for corrosion resistance and lightweight performance.
A solar power system to support autonomous operations.
A sealed electronics compartment and a central mast for sensors, antennas, and GPS.
Designed to withstand harsh marine conditions, including strong currents and waves up to 4 meters.
Solar panel
AIS + GPS
Iridium SDB modem
Anemometer
Power regulator
Embedded fanless computer
Audio Interface
Batery
Analog signal conditioning
Analog signal conditioning
Hydrophone
Hydrophone

---
Layered Architecture of the Embedded System
🔝 Orchestrator Layer
Coordinates overall system flow.
Decides which FSM to activate and when.
Handles high-level internal and external events.
🔁 State Machine Layer (FSM)
Manages module behaviour based on current state.
Responds to events, executes actions, changes states.
⚙️ Low-Level Driver Layer
Interfaces directly with hardware.
Performs device I/O and peripheral configuration.
Task Manager (System Orchestrator)
Event reporting through message queues
Signals to FSM
Finite State Machine (FSM)
Calls to driver methods
Return status
(OK / ERROR)
Low-Level Driver

---
State Machine Design Pattern
This generic FSM pattern is used across multiple modules to manage their internal logic and execution flow.
DISABLE: The module is inactive and resources are released.
INIT: Initializes hardware and internal variables.
TEST: Performs self-checks and verifies correct functionality.
IDLE: Waits for commands or events.
RUN JOB: Executes the main task or acquisition.
ERROR: Captures faults and attempts recovery or shutdown.
Transitions are triggered by internal events or commands from the Task Manager.
Each FSM responds only to relevant signals, ensuring modularity and reuse.
DISABLE
INIT
TEST
ERROR
IDLE
RUN JOB

---
Slide Title goes here [Font: Arial Bold/Size: 22]
[Textbody Font: Arial Regular/ Min. Size: 20]
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua.
Ut enim ad minim veniam, quis nostrud exercitation ullamco laboris nisi ut aliquip ex ea commodo consequat. Duis aute irure dolor in reprehenderit in voluptate velit esse cillum dolore eu fugiat nulla pariatur. Excepteur sint occaecat cupidatat non proident.
***TEXTBODIE(s): max. 400 characters per slide***