## Slide 1
Prario, I. Bos, P. Marques Rojo, R. Cinquini,M. Blanc, S.
Argentinian Navy Research Office & UNIDEF (CONICET)
Presentation Date: 11 September 2025
A Portable Experimental Buoy for Coastal Acoustic Monitoring as a Potential Complement to the IMS Hydroacoustic Network: Applications on the Argentinian Continental Shelf
T1.3 - 299

## Slide 2
Background
Airgun array used in seismic surveys generate sound pulses (5–60 Hz) that can propagate over ocean-basin scales.
Under favourable conditions, signals reach CTBT IMS hydroacoustic (HA) stations with high SNR.
On the Argentinian Continental Shelf, airgun signals detected at H10N can be used to validate long-range propagation models (1).
Limitations: highly directional sources and shallow-water propagation reduce detectability.
Challenge: synchronize ground-truth airgun shots with H10N recordings.
A Portable Experimental Buoy for Coastal Acoustic Monitoring
Prario, I; Bos, P; Marques Rojo, R; Cinquini, M; Blanc, S.
T1.3 - 299
(1) SnT2021 P1.3-494 An inverse problem approach for acoustic Transmission Loss estimation from the analysis of signals generated by seismic air-gun arrays. SnT2023 O1.3-536 Analysis of bathymetric effects on long-range acoustic propagation using 2D and 3D Transmission Loss models in signals generated by airgun arrays.

## Slide 3
Motivation
A Portable Experimental Buoy for Coastal Acoustic Monitoring
Prario, I; Bos, P; Marques Rojo, R; Cinquini, M; Blanc, S.
T1.3 - 299
Offshore Argentina: seismic surveys are conducted in oil & gas exploration blocks.
Large dataset of high-amplitude impulsive signals → basin-scale range propagation analysis.
Airgun array source levels simulated with an open-source airgun modelling software(2); source energy concentrated in 5–70 Hz band (HA10 direction); SL~ 210-190 dB re 1uPa2m2s.
Need for local measurement sites on the Continental Shelf (airgun shots signals & other underwater noise sources).
(2) Sertlek, H. O., and Ainslie, M. A. (2015). “AGORA: Airgun Source Signature Model: Its application for the Dutch Seismic Survey,” in Proceedings of Underwater Acoustics Conference and Exhibition, Crete, Greece, pp. 439–446,

## Slide 4
Acoustic coverage in Argentinian Continental Shelf
A Portable Experimental Buoy for Coastal Acoustic Monitoring
Prario, I; Bos, P; Marques Rojo, R; Cinquini, M; Blanc, S.
T1.3 - 299
Acoustic coverage areas of the HA10 station: preliminary analysis using 2D Parabolic Equation (PE) model RAM (Range-dependent Acoustic Model, Julia implementation).
Acoustic scenario:
Oceanographic databases: T, S profiles from Copernicus; bathymetry from GEBCO.
Frequencies band analyzed: 2–100 Hz.
Transmission Loss (TL) computed along Nx2D radial transects from H10N.
Source depth = 8 m (typical for airgun array).
Coverage criterion: TL < 200 dB; NL ~ 80 dB re 1uPa2 .
Goal: identify candidate shallow-water sites (<200 m depth) for improved local monitoring.

## Slide 5
Offshore Argentina coverage of Ascention station H10N
A Portable Experimental Buoy for Coastal Acoustic Monitoring
Prario, I; Bos, P; Marques Rojo, R; Cinquini, M; Blanc, S.
T1.3 - 299
3 Prario, I., Cinquini, M., Marques Rojo, R. et al. Characterization of the Acoustic Event Associated with the Loss of the ARA San Juan Submarine Based on Long-Range Measurements by CTBTO’s Hydrophone Stations. Pure Appl. Geophys. 180, 1317–1342 (2023). https://doi.org/10.1007/s00024-022-03090-0.
Strong frequency dependence:
Low frequencies (<10 Hz): coastal shadow zones, TL > 200 dB.
Higher frequencies (10–80 Hz): partial coverage, but limited in shallow waters.
Argentine continental slope acts as an acoustic filter.
Coastal coverage gaps: long-range IMS hydroacoustic stations miss nearshore regions.
Local minima of TL in the continental slope (ARA San Juan wreckage, signal of 2017 implosion event was detected in two IMS-HA stations3)
Offshore candidate sites identified: 1-MDQ, 2-CRD

## Slide 6
A Portable Experimental Buoy for Coastal Acoustic Monitoring
Prario, I; Bos, P; Marques Rojo, R; Cinquini, M; Blanc, S.
T1.3 - 299
3 Prario, I., Cinquini, M., Marques Rojo, R. et al. Characterization of the Acoustic Event Associated with the Loss of the ARA San Juan Submarine Based on Long-Range Measurements by CTBTO’s Hydrophone Stations. Pure Appl. Geophys. 180, 1317–1342 (2023). https://doi.org/10.1007/s00024-022-03090-0.
Offshore Argentina coverage of Ascention station H10N
Strong frequency dependence:
Low frequencies (<10 Hz): coastal shadow zones, TL > 200 dB.
Higher frequencies (10–80 Hz): partial coverage, but limited in shallow waters.
Argentine continental slope acts as an acoustic filter.
Coastal coverage gaps: long-range IMS hydroacoustic stations miss nearshore regions.
Local minima of TL in the continental slope (ARA San Juan wreckage, signal of 2017 implosion event was detected in two IMS-HA stations3)
Offshore candidate sites identified: 1-MDQ, 2-CRD

## Slide 7
A Portable Experimental Buoy for Coastal Acoustic Monitoring
Prario, I; Bos, P; Marques Rojo, R; Cinquini, M; Blanc, S.
T1.3 - 299
3 Prario, I., Cinquini, M., Marques Rojo, R. et al. Characterization of the Acoustic Event Associated with the Loss of the ARA San Juan Submarine Based on Long-Range Measurements by CTBTO’s Hydrophone Stations. Pure Appl. Geophys. 180, 1317–1342 (2023). https://doi.org/10.1007/s00024-022-03090-0.
Offshore Argentina coverage of Ascention station H10N
Strong frequency dependence:
Low frequencies (<10 Hz): coastal shadow zones, TL > 200 dB.
Higher frequencies (10–80 Hz): partial coverage, but limited in shallow waters.
Argentine continental slope acts as an acoustic filter.
Coastal coverage gaps: long-range IMS hydroacoustic stations miss nearshore regions.
Local minima of TL in the continental slope (ARA San Juan wreckage, signal of 2017 implosion event was detected in two IMS-HA stations3)
Offshore candidate sites identified: 1-MDQ, 2-CRD

## Slide 8
A Portable Experimental Buoy for Coastal Acoustic Monitoring
Prario, I; Bos, P; Marques Rojo, R; Cinquini, M; Blanc, S.
T1.3 - 299
3 Prario, I., Cinquini, M., Marques Rojo, R. et al. Characterization of the Acoustic Event Associated with the Loss of the ARA San Juan Submarine Based on Long-Range Measurements by CTBTO’s Hydrophone Stations. Pure Appl. Geophys. 180, 1317–1342 (2023). https://doi.org/10.1007/s00024-022-03090-0.
Offshore Argentina coverage of Ascention station H10N
Strong frequency dependence:
Low frequencies (<10 Hz): coastal shadow zones, TL > 200 dB.
Higher frequencies (10–80 Hz): partial coverage, but limited in shallow waters.
Argentine continental slope acts as an acoustic filter.
Coastal coverage gaps: long-range IMS hydroacoustic stations miss nearshore regions.
Local minima of TL in the continental slope (ARA San Juan wreckage, signal of 2017 implosion event was detected in two IMS-HA stations3)
Offshore candidate sites identified: 1-MDQ, 2-CRD

## Slide 9
A Portable Experimental Buoy for Coastal Acoustic Monitoring
Prario, I; Bos, P; Marques Rojo, R; Cinquini, M; Blanc, S.
T1.3 - 299
3 Prario, I., Cinquini, M., Marques Rojo, R. et al. Characterization of the Acoustic Event Associated with the Loss of the ARA San Juan Submarine Based on Long-Range Measurements by CTBTO’s Hydrophone Stations. Pure Appl. Geophys. 180, 1317–1342 (2023). https://doi.org/10.1007/s00024-022-03090-0.
Offshore Argentina coverage of Ascention station H10N
Strong frequency dependence:
Low frequencies (<10 Hz): coastal shadow zones, TL > 200 dB.
Higher frequencies (10–80 Hz): partial coverage, but limited in shallow waters.
Argentine continental slope acts as an acoustic filter.
Coastal coverage gaps: long-range IMS hydroacoustic stations miss nearshore regions.
Local minima of TL in the continental slope (ARA San Juan wreckage, signal of 2017 implosion event was detected in two IMS-HA stations3)
Offshore candidate sites identified: 1-MDQ, 2-CRD

## Slide 10
A Portable Experimental Buoy for Coastal Acoustic Monitoring
Prario, I; Bos, P; Marques Rojo, R; Cinquini, M; Blanc, S.
T1.3 - 299
3 Prario, I., Cinquini, M., Marques Rojo, R. et al. Characterization of the Acoustic Event Associated with the Loss of the ARA San Juan Submarine Based on Long-Range Measurements by CTBTO’s Hydrophone Stations. Pure Appl. Geophys. 180, 1317–1342 (2023). https://doi.org/10.1007/s00024-022-03090-0.
Offshore Argentina coverage of Ascention station H10N
Strong frequency dependence:
Low frequencies (<10 Hz): coastal shadow zones, TL > 200 dB.
Higher frequencies (10–80 Hz): partial coverage, but limited in shallow waters.
Argentine continental slope acts as an acoustic filter.
Coastal coverage gaps: long-range IMS hydroacoustic stations miss nearshore regions.
Local minima of TL in the continental slope (ARA San Juan wreckage, signal of 2017 implosion event was detected in two IMS-HA stations3)
Offshore candidate sites identified: 1-MDQ, 2-CRD

## Slide 11
A Portable Experimental Buoy for Coastal Acoustic Monitoring
Prario, I; Bos, P; Marques Rojo, R; Cinquini, M; Blanc, S.
T1.3 - 299
Acoustic scenario:
Frequency range: 2–100 Hz (results shown at 10, 20, 50, 80 Hz).
Source depth = 8 m (typical airgun tow depth).
Receiver depth (hydrophone) = 40 m.
T, S profiles from Copernicus.
Bathymetry from GEBCO database.
Seabead: sand? Width?
NL~80-85 dB re 1uPa2
Simulation:
2D PE with RAM.jl.
Transmission Loss (TL) along Nx2D radial transects from the candidate hydrophone deployment station.
Objective:
Assess acoustic coverage over the continental shelf and adjacent waters.
Coverage of candidate 1 station (offshore Mar del Plata - MDQ)

## Slide 12
A Portable Experimental Buoy for Coastal Acoustic Monitoring
Prario, I; Bos, P; Marques Rojo, R; Cinquini, M; Blanc, S.
T1.3 - 299
Strong frequency dependence: lower frequencies (10 Hz) show larger shadow zones.
Shelf filtering effect: continental slope reduces transmission at low frequencies (<20 Hz).
Improved coverage at mid–high frequencies (50–80 Hz) across shelf and slope.
Shallow-water gap: limited detectability close to the coast (<200 m depth).
Implication: buoy at MDQ enhances monitoring in northern shelf region.
Coverage of candidate 1 station (offshore Mar del Plata - MDQ)

## Slide 13
A Portable Experimental Buoy for Coastal Acoustic Monitoring
Prario, I; Bos, P; Marques Rojo, R; Cinquini, M; Blanc, S.
T1.3 - 299
Coverage of candidate 1 station (offshore Mar del Plata - MDQ)
Strong frequency dependence: lower frequencies (10 Hz) show larger shadow zones.
Shelf filtering effect: continental slope reduces transmission at low frequencies (<20 Hz).
Improved coverage at mid–high frequencies (50–80 Hz) across shelf and slope.
Shallow-water gap: limited detectability close to the coast (<200 m depth).
Implication: buoy at MDQ enhances monitoring in northern shelf region.

## Slide 14
A Portable Experimental Buoy for Coastal Acoustic Monitoring
Prario, I; Bos, P; Marques Rojo, R; Cinquini, M; Blanc, S.
T1.3 - 299
Coverage of candidate 1 station (offshore Mar del Plata - MDQ)
Strong frequency dependence: lower frequencies (10 Hz) show larger shadow zones.
Shelf filtering effect: continental slope reduces transmission at low frequencies (<20 Hz).
Improved coverage at mid–high frequencies (50–80 Hz) across shelf and slope.
Shallow-water gap: limited detectability close to the coast (<200 m depth).
Implication: buoy at MDQ enhances monitoring in northern shelf region.

## Slide 15
A Portable Experimental Buoy for Coastal Acoustic Monitoring
Prario, I; Bos, P; Marques Rojo, R; Cinquini, M; Blanc, S.
T1.3 - 299
Coverage of candidate 1 station (offshore Mar del Plata - MDQ)
Strong frequency dependence: lower frequencies (10 Hz) show larger shadow zones.
Shelf filtering effect: continental slope reduces transmission at low frequencies (<20 Hz).
Improved coverage at mid–high frequencies (50–80 Hz) across shelf and slope.
Shallow-water gap: limited detectability close to the coast (<200 m depth).
Implication: buoy at MDQ enhances monitoring in northern shelf region.

## Slide 16
A Portable Experimental Buoy for Coastal Acoustic Monitoring
Prario, I; Bos, P; Marques Rojo, R; Cinquini, M; Blanc, S.
T1.3 - 299
Coverage of candidate 2 station (offshore Comodoro Rivadavia - CRD)
Model setup:
Frequency range: 2–100 Hz (results shown at 10, 20, 50, 80 Hz).
Source depth = 8 m (typical airgun tow depth).
Receiver depth (hydrophone) = 40 m.
Environmental inputs:
Oceanographic profiles from Copernicus.
Bathymetry from GEBCO database.
Simulation method:
2D RAM.
Transmission Loss (TL) along radial transects from the candidate buoy site in all directions.
Objective:
Assess acoustic coverage over the continental shelf and adjacent waters.

## Slide 17
A Portable Experimental Buoy for Coastal Acoustic Monitoring
Prario, I; Bos, P; Marques Rojo, R; Cinquini, M; Blanc, S.
T1.3 - 299
Marked frequency variation: stronger attenuation at 10–20 Hz, better propagation at 50–80 Hz.
Continental shelf slope creates coastal shadow zones at low frequencies.
Broader mid-frequency coverage compared to MDQ, extending farther offshore.
Shallow-water limitations remain near coastlines.
Implication: buoy at CRD improves coverage in southern shelf and complements MDQ site.
Coverage of candidate 2 station (offshore Comodoro Rivadavia - CRD)

## Slide 18
A Portable Experimental Buoy for Coastal Acoustic Monitoring
Prario, I; Bos, P; Marques Rojo, R; Cinquini, M; Blanc, S.
T1.3 - 299
Coverage of candidate 2 station (offshore Comodoro Rivadavia - CRD)
Marked frequency variation: stronger attenuation at 10–20 Hz, better propagation at 50–80 Hz.
Continental shelf slope creates coastal shadow zones at low frequencies.
Broader mid-frequency coverage compared to MDQ, extending farther offshore.
Shallow-water limitations remain near coastlines.
Implication: buoy at CRD improves coverage in southern shelf and complements MDQ site.

## Slide 19
A Portable Experimental Buoy for Coastal Acoustic Monitoring
Prario, I; Bos, P; Marques Rojo, R; Cinquini, M; Blanc, S.
T1.3 - 299
Coverage of candidate 2 station (offshore Comodoro Rivadavia - CRD)
Marked frequency variation: stronger attenuation at 10–20 Hz, better propagation at 50–80 Hz.
Continental shelf slope creates coastal shadow zones at low frequencies.
Broader mid-frequency coverage compared to MDQ, extending farther offshore.
Shallow-water limitations remain near coastlines.
Implication: buoy at CRD improves coverage in southern shelf and complements MDQ site.

## Slide 20
A Portable Experimental Buoy for Coastal Acoustic Monitoring
Prario, I; Bos, P; Marques Rojo, R; Cinquini, M; Blanc, S.
T1.3 - 299
Coverage of candidate 2 station (offshore Comodoro Rivadavia - CRD)
Marked frequency variation: stronger attenuation at 10–20 Hz, better propagation at 50–80 Hz.
Continental shelf slope creates coastal shadow zones at low frequencies.
Broader mid-frequency coverage compared to MDQ, extending farther offshore.
Shallow-water limitations remain near coastlines.
Implication: buoy at CRD improves coverage in southern shelf and complements MDQ site.

## Slide 21
Experimental Buoy Platform for hydrophones deployment
This custom-designed buoy is a prototype platform developed for the deployment of hydroacoustic instrumentation in a coastal environment.
It features:
A GRP (Glass-Reinforced Plastic) hull for corrosion resistance and lightweight performance.
A solar power system to support autonomous operations.
A sealed electronics compartment and a central mast for sensors, antennas, satellite transmission and GPS.
Designed to withstand harsh marine conditions, including strong currents and waves up to 4 meters.
A Portable Experimental Buoy for Coastal Acoustic Monitoring
Prario, I; Bos, P; Marques Rojo, R; Cinquini, M; Blanc, S.
T1.3 - 299

## Slide 22
Buoy Electronics Rack
Removable, lift-out aluminum rack houses:
Fanless embedded computer
24-bit audio interface for hydrophone digitization
Low-noise hydrophone preamplifiers
AIS (Automatic Identification System)
Satellite modem for telemetry and command
Deep-cycle battery with solar charge controller
A Portable Experimental Buoy for Coastal Acoustic Monitoring
Prario, I; Bos, P; Marques Rojo, R; Cinquini, M; Blanc, S.
T1.3 - 299

## Slide 23
SCHEMATIC OF THE BUOY MOORING SYSTEM WITH HYDROPHONES
A Portable Experimental Buoy for Coastal Acoustic Monitoring
Prario, I; Bos, P; Marques Rojo, R; Cinquini, M; Blanc, S.
T1.3 - 299

## Slide 24
Layered Architecture of the Embedded System
A Portable Experimental Buoy for Coastal Acoustic Monitoring
Prario, I; Bos, P; Marques Rojo, R; Cinquini, M; Blanc, S.
T1.3 - 299
Task Manager (System Orchestrator)
Finite State Machine (FSM)
Low-Level Driver
Signals to FSM
Event reporting through message queues
Return status (OK / ERROR)
Calls to driver methods
🔝 Orchestrator Layer
Coordinates overall system flow.
Decides which FSM to activate and when.
Handles high-level internal and external events.
🔁 State Machine Layer (FSM)
Manages module behaviour based on current state.
Responds to events, executes actions, changes states.
⚙️ Low-Level Driver Layer
Interfaces directly with hardware.
Performs device I/O and peripheral configuration.

## Slide 25
Layered Architecture of the Embedded System
🔝 Orchestrator Layer
Coordinates overall system flow.
Decides which FSM to activate and when.
Handles high-level internal and external events.
🔁 State Machine Layer (FSM)
Manages module behaviour based on current state.
Responds to events, executes actions, changes states.
⚙️ Low-Level Driver Layer
Interfaces directly with hardware.
Performs device I/O and peripheral configuration.
A Portable Experimental Buoy for Coastal Acoustic Monitoring
Prario, I; Bos, P; Marques Rojo, R; Cinquini, M; Blanc, S.
T1.3 - 299
Task Manager (System Orchestrator)
Finite State Machine (FSM)
Low-Level Driver
Signals to FSM
Calls to driver methods
Event reporting through message queues
Return status (OK / ERROR)

## Slide 26
Layered Architecture of the Embedded System
🔝 Orchestrator Layer
Coordinates overall system flow.
Decides which FSM to activate and when.
Handles high-level internal and external events.
🔁 State Machine Layer (FSM)
Manages module behaviour based on current state.
Responds to events, executes actions, changes states.
⚙️ Low-Level Driver Layer
Interfaces directly with hardware.
Performs device I/O and peripheral configuration.
A Portable Experimental Buoy for Coastal Acoustic Monitoring
Prario, I; Bos, P; Marques Rojo, R; Cinquini, M; Blanc, S.
T1.3 - 299
Task Manager (System Orchestrator)
Finite State Machine (FSM)
Low-Level Driver
Signals to FSM
Event reporting through message queues
Return status (OK / ERROR)
Calls to driver methods

## Slide 27
Layered Architecture of the Embedded System
A Portable Experimental Buoy for Coastal Acoustic Monitoring
Prario, I; Bos, P; Marques Rojo, R; Cinquini, M; Blanc, S.
T1.3 - 299
Task Manager (System Orchestrator)
Finite State Machine (FSM)
Low-Level Driver
Signals to FSM
Event reporting through message queues
Return status (OK / ERROR)
Calls to driver methods
🔝 Orchestrator Layer
Coordinates overall system flow.
Decides which FSM to activate and when.
Handles high-level internal and external events.
🔁 State Machine Layer (FSM)
Manages module behaviour based on current state.
Responds to events, executes actions, changes states.
⚙️ Low-Level Driver Layer
Interfaces directly with hardware.
Performs device I/O and peripheral configuration.

## Slide 28
State Machine Design Pattern
This generic FSM pattern is used across multiple modules to manage their internal logic and execution flow.
DISABLE: The module is inactive and resources are released.
INIT: Initializes hardware and internal variables.
TEST: Performs self-checks and verifies correct functionality.
ERROR: Captures faults and attempts recovery or shutdown.
IDLE: Waits for commands or events.
RUN JOB: Executes the main task or acquisition.
Transitions are triggered by internal events or commands.
Each FSM has a scheduler, message_handler and update functions
A Portable Experimental Buoy for Coastal Acoustic Monitoring
Prario, I; Bos, P; Marques Rojo, R; Cinquini, M; Blanc, S.
T1.3 - 299
DISABLE
INIT
TEST
IDLE
ERROR
RUN JOB

## Slide 29
State Machine Design Pattern
This generic FSM pattern is used across multiple modules to manage their internal logic and execution flow.
DISABLE: The module is inactive and resources are released.
INIT: Initializes hardware and internal variables.
TEST: Performs self-checks and verifies correct functionality.
ERROR: Captures faults and attempts recovery or shutdown.
IDLE: Waits for commands or events.
RUN JOB: Executes the main task or acquisition.
Transitions are triggered by internal events or commands.
Each FSM has a scheduler, message_handler and update functions
A Portable Experimental Buoy for Coastal Acoustic Monitoring
Prario, I; Bos, P; Marques Rojo, R; Cinquini, M; Blanc, S.
T1.3 - 299
DISABLE
INIT
TEST
IDLE
ERROR
RUN JOB

## Slide 30
State Machine Design Pattern
This generic FSM pattern is used across multiple modules to manage their internal logic and execution flow.
DISABLE: The module is inactive and resources are released.
INIT: Initializes hardware and internal variables.
TEST: Performs self-checks and verifies correct functionality.
ERROR: Captures faults and attempts recovery or shutdown.
IDLE: Waits for commands or events.
RUN JOB: Executes the main task or acquisition.
Transitions are triggered by internal events or commands.
Each FSM has a scheduler, message_handler and update functions
A Portable Experimental Buoy for Coastal Acoustic Monitoring
Prario, I; Bos, P; Marques Rojo, R; Cinquini, M; Blanc, S.
T1.3 - 299
DISABLE
INIT
TEST
IDLE
ERROR
RUN JOB

## Slide 31
State Machine Design Pattern
This generic FSM pattern is used across multiple modules to manage their internal logic and execution flow.
DISABLE: The module is inactive and resources are released.
INIT: Initializes hardware and internal variables.
TEST: Performs self-checks and verifies correct functionality.
ERROR: Captures faults and attempts recovery or shutdown.
IDLE: Waits for commands or events.
RUN JOB: Executes the main task or acquisition.
Transitions are triggered by internal events or commands.
Each FSM has a scheduler, message_handler and update functions
A Portable Experimental Buoy for Coastal Acoustic Monitoring
Prario, I; Bos, P; Marques Rojo, R; Cinquini, M; Blanc, S.
T1.3 - 299
DISABLE
INIT
TEST
IDLE
ERROR
RUN JOB

## Slide 32
State Machine Design Pattern
This generic FSM pattern is used across multiple modules to manage their internal logic and execution flow.
DISABLE: The module is inactive and resources are released.
INIT: Initializes hardware and internal variables.
TEST: Performs self-checks and verifies correct functionality.
ERROR: Captures faults and attempts recovery or shutdown.
IDLE: Waits for commands or events.
RUN JOB: Executes the main task or acquisition.
Transitions are triggered by internal events or commands.
Each FSM has a scheduler, message_handler and update functions
A Portable Experimental Buoy for Coastal Acoustic Monitoring
Prario, I; Bos, P; Marques Rojo, R; Cinquini, M; Blanc, S.
T1.3 - 299
DISABLE
INIT
TEST
IDLE
ERROR
RUN JOB

## Slide 33
State Machine Design Pattern
This generic FSM pattern is used across multiple modules to manage their internal logic and execution flow.
DISABLE: The module is inactive and resources are released.
INIT: Initializes hardware and internal variables.
TEST: Performs self-checks and verifies correct functionality.
ERROR: Captures faults and attempts recovery or shutdown.
IDLE: Waits for commands or events.
RUN JOB: Executes the main task or acquisition.
Transitions are triggered by internal events or commands.
Each FSM has a scheduler, message_handler and update functions
A Portable Experimental Buoy for Coastal Acoustic Monitoring
Prario, I; Bos, P; Marques Rojo, R; Cinquini, M; Blanc, S.
T1.3 - 299
DISABLE
INIT
TEST
IDLE
ERROR
RUN JOB

## Slide 34
State Machine Design Pattern
This generic FSM pattern is used across multiple modules to manage their internal logic and execution flow.
DISABLE: The module is inactive and resources are released.
INIT: Initializes hardware and internal variables.
TEST: Performs self-checks and verifies correct functionality.
ERROR: Captures faults and attempts recovery or shutdown.
IDLE: Waits for commands or events.
RUN JOB: Executes the main task or acquisition.
Transitions are triggered by internal events or commands.
Each FSM has a scheduler, message_handler and update functions
A Portable Experimental Buoy for Coastal Acoustic Monitoring
Prario, I; Bos, P; Marques Rojo, R; Cinquini, M; Blanc, S.
T1.3 - 299
DISABLE
INIT
TEST
IDLE
ERROR
RUN JOB

## Slide 35
Conclusions
A Portable Experimental Buoy for Coastal Acoustic Monitoring
Prario, I; Bos, P; Marques Rojo, R; Cinquini, M; Blanc, S.
T1.3 - 299
A low-cost prototype buoy for coastal acoustic monitoring is under integration, designed for robustness and autonomous operation.
The system complements IMS hydroacoustic stations by addressing shallow-water coverage gaps on the Argentine continental shelf.
Proposed deployment sites (MDQ and CRD) optimise detection in previously uncovered regions.
This platform paves the way for a scalable coastal monitoring system supporting baseline studies of ambient underwater noise and long-range propagation analysis.